## Slide 1
The golf course mowing robot
GROUNDSBOT
The A Team:
David Evans
Adam Driscoll
Josh Bennett
Joe Phaneuf
Henry Chen
Sponsor:
Notes: Good afternoon!
We are Team A...But you can call us the A-Team
Our team members are David Evans, Adam Driscoll, Henry Chen, Josh Bennett, and myself, Joe Phaneuf
Our gracious and steadfast sponsor is Discovery Robotics
Today we're going to introduce you to the future of autonomous grounds maintenance....
This. Is. GroundsBot!

## Slide 2: Functional Requirements
GroundsBot shall:
ID | Requirement
F.R.1 | Accept boundaries from user
F.R.2 | Cut the rough at desired quality
F.R.3 | Avoid obstacles
F.R.4 | Climb hills
F.R.5 | Return to home

## Slide 3: Performance Requirements
ID | Requirement
M.P.1 | First time user inputs map within 15 minutes
M.P.2 | System returns proposed route/coverage map within 5 minutes
M.P.3 | Cover 1/4 acre in 30 minutes on flat, unobstructed terrain
M.P.4 | Cut 0-25% overlap for 95% of grass
M.P.5 | Navigate 30 degree sloped grass
M.P.6 | Detect 80% of static objects greater than 3 inches in height and 2 inches in width
M.P.7 | Detect 80% of dynamic objects greater than 6 inches in height and 6 inches in width travelling less than 4 mph
M.P.8 | Mow to within 1 foot of detected obstacles
M.P.9 | Return home to within 5 feet of starting position
GroundsBot will:
Notes: Adam

## Slide 4: Non-functional Requirements
ID | Requirement
M.N.1 | Have a functional and easily accessible emergency stop
M.N.2 | Be clearly visible
M.N.3 | Not tear up grass
GroundsBot will:
Notes: Adam

## Slide 5: Functional Architecture
Notes: Josh

## Slide 6: Cyber-physical Architecture
Notes: Josh

## Slide 7: SVE WBS
Planning | Mapping | Control | Management
Mission Planner | Obstacle mapping | Motor control | Schedule
Local motion Planner | Boundary correction |  | Finance
 |  |  | Risk
 |  |  | Personnel
UI | Platform | Localization | Perception
App | Electronics | Global localization | Grass (type) detection
 | Chassis | Obstacle localization | Static obstacle detection
 | Firmware |  | Dynamic obstacle detection
Notes: Joe

## Slide 8: FVE WBS Part 1
Notes: Joe

## Slide 9: FVE WBS Part 2
Notes: Joe

## Slide 10: Schedule
Notes: Joe

## Slide 11: Risks
Risk | Description | Management Strategy | Risk Category
Not Enough Capital for Development: | There is a risk our system requires more money than initially allocated. | Maintain strong relationship with sponsor Reach out to other sponsors or donors Strictly monitor budgeted plan | Schedule
Injury from Spinning Blade: | Our system has a dangerous cutting instrument. It can injure a team member or a bystander. | Make sure team understands risk of testing system Safety tether or switch to shut off mower immediately Put warning lights and sounds to alert bystanders | Technical
Subsystem Harder Than Expected: | Any subsystem could require more work than expected, taking away focus from other subsystems. | Focusing on critical subsystems first, to mitigate failure Revise scope related to subsystem if necessary Budget extra time for extended effort | Technical
Notes: Henry

## Slide 12
Notes: Questions?