## Slide 1
The golf course mowing robot
GROUNDSBOT
The A Team:
David Evans
Adam Driscoll
Josh Bennett
Joe Phaneuf
Henry Chen
Sponsor:
Notes: Joe

## Slide 2
Demonstrate user interface
Demonstrate mowing coverage %
Demonstrate coverage rate
Demonstrate handling on slopes
Demonstrate ability to avoid static obstacles
Demonstrate ability to avoid dynamic obstacles
Test Objectives
Notes: Joe

## Slide 3
SVE Test 1
Objective: Demonstrate User Interface and Static Obstacle Detection
Notes: Joe

## Slide 4
Objective: Demonstrate GroundsBot’s dynamic obstacle detection
SVE Test 2
Notes: Adam
Key point. GroundsBot should reroute around STATIC obstacles, but will just stop if a dynamic obstacle is detected

## Slide 5
Objective: Demonstrate that GroundsBot can operate on sloped regions
SVE Test 3
Notes: Josh

## Slide 6
Objective: Validate GroundsBot’s mowing coverage and coverage rate
SVE Test 4
Notes: Offline
Henry

## Slide 7: Questions for the audience?
Coverage rate and coverage percentage split from test 1?
How do we measure coverage?
Split dynamic and static obstacle testing make sense?
Does hill test show GroundsBot can handle hills?

## Slide 8
Stereo Camera
Detect Static Obstacles
Detect Dynamic Obstacles
Generate
Map
Local
Planner
Global
Planner
Platform
Boundary Input
Display Mowing Plan
Localize Position
Polygon Boundary
Mowing Plan
Pose Estimate
Velocity Commands
GPS Waypoints
Local Costmap
Point Cloud
U/I Subsystem
Perception Subsystem
Navigation Subsystem
Log Map
Display Mowing Status
GroundsBot
Software
Architecture
(with logging infrastructure)
Notes: David

## Slide 9: Questions for the audience?
Does this logically make sense?
Does anyone have any experience generating costmaps?
Global planner, local planner relationship? Right now the global planner does not update over time, it only provides a set of GPS waypoints at the beginning. Does this make sense?

## Slide 10
M.P.1, First time user inputs map within 15 minutes
M.P.2, System returns proposed route/coverage map within 5 minutes
M.P.3, Cover 1/4 acre per hour on flat, unobstructed terrain
M.P.4, Cut 95% of the grass on flat, unobstructed terrain
M.P.5, Navigate 30 degree sloped grass
M.P.6 , Detect 80% of static objects greater than 3 inches in height and 2 inches in width
M.P.7 , Detect 80% of dynamic objects greater than 6 inches in height and 6 inches in width travelling less than 4 mph
M.P.8 , Mow to within 1 foot of detected obstacles
M.P.9 , Return home to within 5 feet of starting position
Requirements:

## Slide 11
1. Obstacle Officer places new obstacles until test site contains a total of 5 obstacles 2. Obstacle Officer places Yellow cone as home position marker 3. GroundsBot Technician holds GroundsBot safety tether and follows GroundsBot for duration of test 4. GroundsBot Technician powers on GroundsBot. 5. Technical Sales Rep opens UI on laptop and establishes a connection with GroundsBot 6. Technical Sales Rep briefs New User on app functionality 7. New User uses UI on laptop to define boundaries of area to be mowed through the UI 8. New User uses UI on laptop to submit the mowing area to GroundsBot 9. GroundsBot develops a coverage plan 10. GroundsBot mows the area 11. GroundsBot returns to its starting position 12. New user receives coverage report on laptop UI 13. Obstacle Officer measures and records distances from mowed grass to obstacles 14. Obstacle Officer measures and records distance from GroundsBot to home position
SVE Test 1: Procedure

## Slide 12
Verification Criteria
M.P.1, First time user inputs map within 15 minutes
M.P.2, System returns proposed route/coverage map within 5 minutes
M.P.6 , Detect 80% of static objects greater than 3 inches in height and 2 inches in width
M.P.8 , Mow to within 1 foot of detected obstacles
M.P.9 , Return home to within 5 feet of starting position
D.P.1 , Mow to within 3 inches of a detected obstacles
D.P.2 , Visually report mowing coverage and obstacles encountered
M.N.2 , Be clearly visible , GroundsBot should indicate its presence and status to everyone nearby
SVE Test 1: Validation Criteria

## Slide 13
Objective: Validate GroundsBot’s dynamic obstacle detection
Procedure
Power on GroundsBot
Open UI and establish connection with GroundsBot
Team member creates a straight line path for GroundsBot to follow using the UI
Team member enables GroundsBot and GroundsBot starts moving along path
Rest of team lines up along path GroundsBot is following
As GroundsBot approaches team member uses calibrated GrudsMeter® to roll a soccer ball in front of GroundsBot as per requirements
When soccer ball enters line of sight Groundsbot will stop
When soccer ball leaves line of sight Groundsbot will continue along its original path
Repeat steps 6-8 four more times.
SVE Test 2

## Slide 14
SVE Test 2
Verification Criteria
M.P.7 - Detect 80% of dynamic objects greater tha6 inches in height and 6 inches in width travelling less than 4 mph
GroundsBot detects a moving obstacle
GroundsBot stops moving until the obstacle has left line of sight. Groundsbot will come to a full stop for ⅘ dynamic obstacles.
Once obstacle has left line of sight, GroundsBot continues moving along original path

## Slide 15
Procedure
Surveyor measures test site and marks region containing 30 degree slope with cones
Cinematographer begins recording
Operator navigates GroundsBot straight up 30 degree slope
Cinematographer ends recording
SVE Test 3

## Slide 16
Verification Criteria
M.P.5, Navigate 30 degree sloped grass
SVE Test 3

## Slide 17
Procedure
Cinematographer 1 initializes static camera position and begins recording
Cinematographer 2 begins recording and follows GroundsBot
Operator navigates GroundsBot to home position using RC transmitter
Operator launches mission and Time Cop starts stopwatch
GroundsBot completes mission and returns home and Time Cop stops stopwatch
Surveyor bounds and measures failed coverage with stakes and tape measure
Cinematographers 1 and 2 end recording
SVE Test 4

## Slide 18
Verification Criteria
M.P.3: Cover 1/8 acre per 30 minutes on flat, unobstructed terrain
M.P.4: Cut 95% of the grass on flat, unobstructed terrain
M.N.3: Do not tear up grass
SVE Test 4

## Slide 19
Stereo Camera
Detect Static Obstacles
Detect Dynamic Obstacles
Generate
Map
Local
Planner
Global
Planner
Platform
Boundary Input
Display Mowing Plan
Localize Position
Polygon Boundary
Mowing Plan
Pose Estimate
Velocity Commands
GPS Waypoints
Local Costmap
U/I Subsystem
Point Cloud
Perception Subsystem
Navigation Subsystem
GroundsBot
Software
Architecture